## Slide 1: Through the River and Over the Woods – Global PFAS Exposure and Implications for Ecosystem Health
Lisa McIntosh, MS, DABT
Woodard & Curran, Inc.
Soil and Water Conservation Society
Southern New England Chapter
March 30, 2023

## Slide 2: What are PFAS?
Per- and Polyfluoroalkyl Substances
Large class of man-made compounds
  Very stable, carbon-fluorine bonds
  High thermal, chemical stability
  Water soluble
Used as surfactants, water/stain repellents, etc.
C – F
4-eva

## Slide 3: Environmental focus on perfluoroalkyl group
Nonpolymers
Cn F2n+1 – R
Perfluoroalkyl carboxylic acids (PFCAs) - PFOA
Perfluoroalkyl sulfonic acids (PFSA) – PFOS
Long vs. short chain
Some polyfluoroalkyl substances also important
  Precursors to PFCAs
    fluorotelomers
Persistent, Bioaccumulative, Toxic
PFOA: Perfluorooctanoic acid (C8)
PFOS: Perfluorooctane sulfonic acid
Notes: Focus is on PFAAs because most commonly detected in environment, in most PFAS analyte lists currently; have tox data for humans/ecological receptors, federal guidance values/criteria
PFOA has carboxyl functional group, PFOS has sulfonic acid
Polyfluoroalkyl substances – in particular, fluoroteomers, may degrade into PFCAs and so may be significant source in the environment.

## Slide 4: PFAS Sources/Uses
Fire-fighting foams (e.g., AFFF)
Consumer products
Industrial use
  Aerospace, metal plating, automotive, electronics, construction, etc.
Source: Riverside Public Utilities
https://riversideca.gov/press/understanding-pfas
Notes: AFFF – aqueous film forming foam
Graphic from California’s Riverside Public Utilities

## Slide 5: How do PFAS move through the environment?
Leaching to groundwater
Migration to surface water
Landfilling
Bioaccumulation

## Slide 6: PFAS in the air
Important transport system
  Local and global
  Gas, aerosol, particulates
  Volatile precursors can be prevalent
Removal via deposition
  Dry particulates
  Precipitation
Source: ITRC PFAS Technical and Regulatory Document
https://pfas-1.itrcweb.org/6-media-specific-occurrence/#figure_6_1a
Notes: So – talking about exposure in the environment
Picograms per cubic meter

## Slide 7: Raining down
1H,1H,2H,2H-Perfluorooctanesulfonic Acid (6:2FTS)
Perfluorobutanoic Acid (PFBA)
Perfluorohexanoic Acid (PFHxA)
Perfluorononanoic Acid (PFNA)
Perfluoropentanoic Acid (PFPeA)
% Detected
6%
13%
2%
2%
6%
Minimum Detected
1.82
2.3
1.94
2.86
2.08
Maximum Detected
3.48
3.36
1.94
2.86
2.35
Results in ng/l
Fluorotelomer precursor
Short chain
Woodard & Curran PFAS in Rain Study (unpublished data)
Notes: Highest total PFAS 8.78 ng/l
6:2 FTS – PFOS alternative -mist suppressant in chromate plating process

## Slide 8: PFAS on the ground
PFOS Background Concentrations in New England Soils
Unpublished data
Notes: Part per billion levels

## Slide 9: …and in the ground(water)
Source: Environmental Working Group
https://www.ewg.org/interactive-maps/pfas_contamination/map/
Notes: Soil leaching to groundwater
Variable concentrations, depends on source areas (like military installations or firefighting training areas)
Map: environmental working group

## Slide 10: …and waterways
Direct inputs from atmosphere, wastewater, releases etc.
Indirect input via groundwater, stormwater runoff
Remote areas: pg/L to ng/L

## Slide 11: PFAS transport through the food web
Source: EPA EcoBox: https://www.epa.gov/ecobox/epa-ecobox-tools-exposure-pathways-exposure-pathways-era
Bioconcentration:
Uptake from water
Bioaccumulation:
Uptake from all surrounding sources
Biomagnification:
Increasing concentrations with increasing trophic levels

## Slide 12: PFAS accumulate in biota
Binds to proteins, phospholipids
PFOS predominant
Global exposure documented
Chart: Average PFAS Concentrations By Fish Species, Fillet
| PFNA | PFDA | PFUnA | PFDoA | PFTrDA | PFTeDA | PFHxS | PFHpS | PFOS | PFNS | PFDS | PFDoS | 6:2 FTS | PFOSA | MeFOSAA
Yellow Perch | 0.45456 | 1.4039 | 2.5517 | 2.2772 | 2.3783 | 1.6589 | 0 | 0.11827 | 40.1239 | 0.15493 | 0.47909 | 0 | 0 | 0.43114 | 0
White Sucker | 0.35091 | 0.71755 | 1.5428 | 0.77155 | 1.1831 | 0.50328 | 0.11107 | 0 | 19.8859 | 0.21461 | 0.40897 | 0 | 0 | 0.57507 | 0.12501
Notes: Part per billion levels

## Slide 13: Bioaccumulation is highly variable
C8
PFOS
C10
PFDS
C3
PFBA
More bioaccumulative
More bioaccumulative
Structure
Media chemistry
Organism
Notes: ‘sweet spot’ of ~C7-C13 for animals
Shorter chain for plants
Highly variable, though

## Slide 14: The Big Question: does exposure translate into effect?
Decades and multitude of laboratory data
Mostly on PFOS and PFOA
Mostly laboratory studies
Toxicity is highly variable among organisms
Notes: EPA Ecotox database

## Slide 15: Health effects in mammals
  Cancer
    PFOA: liver, testicular, pancreatic, kidney
    PFOS: bladder, prostate, kidney, breast
Graphics reproduced from
North Carolina NC PFAST Network:
https://ncpfastnetwork.com/printed-materials/

## Slide 16: Effects on non-mammals
Studies mainly focus on survival, growth, and reproduction
  ppb to ppm levels
  immune, developmental
  transgenerational
Highly variable
Moderation by TOC and other factors

## Slide 17: What don’t we know?
Toxicity of most PFAS
Toxicity in most species
Toxicity of PFAS mixtures
Modulation by environmental factors
Population-level impacts

## Slide 18: Ecological risk assessment of PFAS
Stressors
Migration pathways
Exposure routes
Exposure potential
Toxicity
Risk
Uncertainty

## Slide 19: PFAS ecological benchmarks for surface water
Many states promulgated or are in process of developing WQC
USEPA proposed invertebrate/fish tissue-based NRWQC
Ecological Screening Value | Concentration ug/L | 
 | PFOS | PFOA
USEPA NRWQC-chronic (draft) | 8.4 | 94
Ecological Screening Value1 | 22.6 | 307
1. Grippo, M., Hayse, J. , Hlohowskyj, I. and Picel, K. September 2021. Derivation of PFAS Ecological Screening Values. Argonne National Laboratory
Notes: Argonne National Laboratory, in support of Air Force, developed screening levels for water – part per billion
States: Michigan, Minnesota . Massachusetts has target surface water level to develop groundwater gw-3 criteria.

## Slide 20: PFAS ecological benchmarks for soil
Receptor | Ecological Screening Value (ug/kg)1 | 
 | PFOS | PFOA
Plants | 40,200 | 79,500
Invertebrates | 48,100 | 22,400
Mammals | 8.7 | 3,840
Birds | 38.6 | --
Grippo, M., Hayse, J. , Hlohowskyj, I. and Picel, K. September 2021. Derivation of PFAS Ecological Screening Values. Argonne National Laboratory

## Slide 21: Use multiple lines of evidence to assess risk
Chemistry
Toxicology
Ecology
Risk Characterization
Literature tox values
Lab toxicity studies
Bioaccumulation testing
Abiotic concentrations
Reference levels
Tissue samples
Population surveys
Condition indices
Weight of Evidence is Critical
??
??
??

## Slide 22: Understand limitations and uncertainties
Line of Evidence | Uncertainties
Benchmarks | Few currently available; not site-specific
Toxicity Testing | Which species is most sensitive?
Bioaccumulation Testing / Tissue Sampling | Standardized analytical methods lacking
Food Chain Models | How to best predict uptake?
Field Surveys | Chemical, physical and biological confounders

## Slide 23: So what does all this mean?
PFAS are prevalent in our environment.
  Organisms are exposed to PFAS on a global scale.
Exposure associated with adverse effects at environmental levels
  Considerable uncertainty/variability

## Slide 25: Have any good news?
PFAS is a priority
  Regulatory impetus
Phase out of PFOS/PFOA
  Human PFOS and PFOA serum levels have decreased
Push for:
  Research & Development
  Analysis
  Remediation
EPA’s PFAS Action Plan, 2019:
“Ecological toxicity information is also needed by stakeholders to inform risk assessment and management to protect ecosystems, animals, and plant resources they support ….”

## Slide 26: PFAS resources
USEPA PFAS Website: https://www.epa.gov/pfas
Interstate Technology and Regulatory Council (ITRC): PFAS Technical and Regulatory Document: https://pfas-1.itrcweb.org/
Argonne National Laboratories, Grippo, M., Hayse, J. , Hlohowskyj, I. and Picel, K. September 2021. Derivation of PFAS Ecological Screening Values. https://www.denix.osd.mil/dodepa/
National Groundwater Association
  Groundwater and PFAS: State of Knowledge and Practice. https://my.ngwa.org/NC__Product?id=a183800000kbKF9AAM
Vermont Soil Study: https://anrweb.vt.gov/PubDocs/DEC/PFOA/Soil-Background/PFAS-Background-Vermont-Shallow-Soils-03-24-19.pdf
Maine Soil Study: https://www.maine.gov/dep/spills/topics/pfas/Maine_Background_PFAS_Study_Report.pdf
New Hampshire Soil Study (data): https://www.usgs.gov/data/statewide-survey-shallow-soil-concentrations-and-polyfluoroalkyl-substances-pfas-and-related

## Slide 27: Thank You!
Questions?
Lisa McIntosh
Woodard & Curran
lmcintosh@woodardcurran.com